## Slide 1
1. Problem statement understanding
PS 8: Smart way to find machine problems early
Speaking
Rajkishor Kushwaha
Spindle Nadi: predicting the machine’s "Last Good Hour" |
The problem
CNC machines and 3D printers in labs stop without warning. Student projects stop. Repairs cost money.
Why the old way fails
Labs check by hand or use one fixed alarm limit. It rings by mistake when the machine is busy, or too late.
Our answer: Spindle Nadi
Like a doctor checks a pulse (Nadi), we check the machine’s pulse: heat, shaking, power use, speed and how hard it works. We find slow damage early and say how many hours are left.
Example: same heat, different meaning
Machine | Fixed alarm (65°C) | Spindle Nadi
90% work, 70°C | Rings. Wrong! | Normal. Heat is expected.
30% work, 70°C | Rings | Warning. Too hot for light work.
Same temperature. The fixed alarm cannot tell the difference. Spindle Nadi can.
Notes: Rajkishor: Good evening, judges. We are Team Spindle Nadi, Problem Statement 8. Machines like CNC routers and 3D printers do not break suddenly. They wear out slowly. Today labs check by hand or use one fixed alarm limit. Look at our example: a machine working at 90 percent is at 70 degrees. A fixed alarm at 65 rings, but the machine is fine. Spindle Nadi knows heat is normal at that work level, so it says Normal. If the machine is only at 30 percent work and still 70 degrees, that is a real problem, so we say Warning. Like a doctor checking a pulse, Spindle Nadi finds trouble hours before the machine breaks.

## Slide 2
2. Approach and technical feasibility
Simple pipeline. Common Python tools. We can build it.
Speaking
Raushan Ali + Aakash Barnawal
Spindle Nadi: predicting the machine’s "Last Good Hour" |
1. Make data
Simulator makes 3 states: Normal, Getting Worse, Near Failure
2. Fix for workload
Hard work is not a fault. Fewer false alarms
3. AI checks
Isolation Forest finds odd signals. XGBoost gives a risk score
4. Show result
Risk 0-40% Normal, 40-70% Warning, 70-100% Critical
Real standard: ISO 10816
Shaking speed (mm/s), small machine:
Under 1.8 = Normal
1.8 to 4.5 = Warning
Over 4.5 = Critical
Tells you WHY
Example result:
Risk 78% = Critical
52% of risk: bearing shaking
30% of risk: motor power use
18% of risk: heat
Can we build it? Yes
100% software.
Python, scikit-learn, XGBoost, Streamlit, Plotly.
Later, real sensors can plug in.
Notes: Raushan: When a machine part called a bearing wears out, it shakes more. We do not guess limits. We use the ISO 10816 world standard for shaking speed. For a small machine, under 1.8 millimeters per second is Normal, 1.8 to 4.5 is Warning, and over 4.5 is Critical. Our physics model makes real-looking data for three states, so we can estimate the Last Good Hour. Aakash: First we fix sensor values for workload, so a busy machine does not cause a false alarm. Then Isolation Forest finds odd signals and XGBoost gives a risk score from 0 to 100 percent. Up to 40 is Normal, 40 to 70 is Warning, above 70 is Critical. Our WHY engine shows the cause. Here, risk is 78 percent, and 52 percent of it comes from bearing shaking. Everything is software, so we can build it in 24 hours.

## Slide 3
3. Development planning
24 hours. 4 phases. 4 people.
Speaking
Hritu Raj Thakur
Spindle Nadi: predicting the machine’s "Last Good Hour" |
Hours 0-6
Set up project, data simulator
Hours 6-12
Train AI, risk score, first dashboard
Hours 12-18
WHY panel, ISO rules, repair history
Hours 18-24
Test 3 states, backup video, practice
Rajkishor Kushwaha (AIDS)
Dashboard and Charts
Raushan (Civil)
wear physics
Aakash (AIML)
AI models, WHY engine
Hrituraj Thakur (CSE)
Pitch testing and emo
24 hours
4 phases
4 team members
3 machine states tested
Notes: Hritu: We have 24 hours and 4 phases of 6 hours each. First 6 hours: set up the project and the data simulator. Next 6 hours: train the AI and build the first dashboard with charts and status badges. Then 6 hours for the WHY panel, ISO rules and repair history. Last 6 hours: test all 3 machine states, record a backup video, and practice. There are 4 of us and each owns one area: Raushan does the physics, Aakash the AI, Rajkishor the dashboard, and I do the pitch and testing. We are on schedule for a working prototype for Review 2. Thank you!